Arduino Nano Bootloader Update
www.binaria.co.uk
How to… and why you might want/need to!
ILN 2022

---
What is the Bootloader?
- It is a small piece of code that runs when the Nano is powered up or reset.
- It checks to see if a new sketch is being sent, else it runs the existing sketch in flash memory.

---
Why Update the Nano Bootloader?
- The “old” bootloader has a bug that prevents the Watchdog Timer from working properly.
- The “old” bootloader is bigger than the new one, so after updating, more flash memory (1.5KB) can be available for sketches. *
- The new bootloader allows faster uploads as it uses 115200 baud – the “old” bootloader uses 57600 baud.
    * If you also fix the high fuses.

---
How to Update the Nano Bootloader
- Verify the Nano has the “old” bootloader.
- Set up an Arduino Uno as “Arduino as ISP”.
  Why use an Uno as the programmer?
  - It has the newer bootloader with 115200 baud.
  - It is not a Nano, so the programmer and the programmed are obvious.
- Connect the Uno to the Nano – just 6 wires needed.
- Adjust the Nano high fuses (in “boards.txt”).
- Restart the IDE and burn the new Nano bootloader.
- Verify the Nano bootloader update.

---
Illustrating the Nano WDT Issue
- Specifically written sketch that triggers the watchdog timer and resets the Arduino.
- The WDT test works as expected on an Uno.
- It does not work on a Nano with the “old” bootloader.
- And, the Nano must be re-powered to recover!
- The sketch has a hardware option to disable the WDT test.
  - Connect pin 2 to GND to disable the WDT test.

---
An Uno as “Arduino as ISP”
- Connect the Uno to the PC.
- Set the Uno as the IDE target board.
- Select to correct serial port.
- Upload the “ArduinoISP” example sketch.
- Monitoring the Uno ISP activity (optional):
  - Uno pin D7 – Programming: LED to a 330Ω resistor to GND.
  - Uno pin D8 – Error: LED to a 330Ω resistor to GND.
  - Uno pin D9 – Heartbeat: LED to a 330Ω resistor to GND.

---
Connect the Uno to the Nano
- Uno pin D10	→ Orange wire to Nano ICSP pin 5 (RST).
- Uno pin D11	→ Yellow wire to Nano ICSP pin 4 (MOSI).
- Uno pin D12	→ Green wire to Nano ICSP pin 1 (MISO).
- Uno pin D13	→ Blue wire to Nano ICSP pin 3 (SCK).
- Uno +5V	→ Red wire to Nano ICSP pin 2 (+5V).
- Uno GND	→ Brown wire to Nano ICSP pin 6 (GND).
  (! this is how my Uno and Nano are connected !)

---
Connecting the Uno to the Nano
Nano	Uno
ICSP #1 MISO	D12
ICSP #2 +5V	+5V
ICSP #3 SCK	D13
ICSP #4 MOSI	D11
ICSP #5 RST	D10
ICSP #6 GND	GND

---
Adjust the Nano High Fuses
- Backup the “boards.txt” file!
- In “boards.txt”, fix some “not old” Nano entries:
  - Max flash size, 30720 → 32256
  (nano.menu.cpu.atmega328.upload.maximum_size=32256)
  - High Fuses, 0xDA → 0xDE
  (nano.menu.cpu.atmega328.bootloader.high_fuses=0xDE)
  - Copy the equivalent numbers from the Uno entry!
- Restart the Arduino IDE for it to see the updates!

---
Burning the New Nano Bootloader
- Turn on verbose output during upload.
- Select the programmer “Arduino as ISP”.
- Set the Nano as the IDE target board.
- Set the processor to “ATmega328P”.
- Check the Uno serial port is still selected.
- Burn the bootloader.
- Change the programmer back to “AVRISP MkII”.

---
Has the Update Worked?
- Lets retry the WDT test script on a Nano.
- Set up the IDE board, processor and serial port.
- Upload the WDT test script again.
  - Flash memory is cleared during the bootloader update!
  - Does the Nano now connect at 115200?
  - Is there more flash memory available for sketches?
  Finally...
- Is the WDT test script working correctly on the Nano?

---
Hurrah! Success!
- But please remember:
  All information was accurate at the time of recording.
  It worked for me, but everything is at your own risk!
- Good luck